## Slide 1: Fruit Quality Classifier using Machine Learning
Ηλίας Αλεξανδρόπουλος mtn2302
Σπυρίδων Γεωργούλας mtn2309
Βασιλική Ρέντουλα mtn2317

## Slide 2: Introduction
Apply advanced machine learning algorithms for fruit quality assessment.
Utilize the FruitNet: Indian Fruits Dataset [1] with Quality for model training.
Develop classification models to categorize fruits by quality indicators.
Optimize model performance for accurate quality categorization.
https://www.kaggle.com/datasets/shashwatwork/fruitnet-indian-fruits-dataset-with-quality?resource=download
[1]

## Slide 3: Data description
3 Sub-folders:
[1]
[1]
https://www.kaggle.com/datasets/shashwatwork/fruitnet-indian-fruits-dataset-with-quality?resource=download
[1]

## Slide 4: Data pre-processing
Background reduction:
exclude unnecessary information
GrabCut algorithm
Feature Extraction:
Color Features (HSV Color Space)
Texture Features (Local Binary Pattern - LBP)
Shape Features (Contours)

## Slide 5: Model Training and Validation
1. 90°rotation 2. 180°rotation 3. 270°rotation 4. Gamma 0.2 5. Gamma 1.2
Hyperparameter tuning SVM
Data: training (80%) and testing (20%)
Randomize order to prevent bias
Unbalanced dataset
Solve: Trimming and Augmentation
C: [0.1, 0.5, 1, 10] to find optimal balance
gamma: [scale, auto, 0.1, 0.01, 0.001, 0.0001] to fine-tune the models' sensitivity

## Slide 6: SVM Models Evaluation
(Linear, Radial Basis Function (RBF), Polynomial, Sigmoid)
Kernel: rbf
C: 10
Class_weight: balanced
Gamma: scale
Accuracy: 0.89
F1 : 0.89

## Slide 7: Evaluation – Comparison model (KNN)

## Slide 8: Evaluation – Comparison model (Decision tree)

## Slide 9: System Integration pipeline

## Slide 10: System Integration
Raspberry Pi Model: Raspberry Pi 3 Model B Camera Module: Raspberry Pi Camera Board v1.3 (5MP, 1080p)
Button

## Slide 11: Thanks!